## Slide 1
Milestone

## Slide 2
Generic Overview
Market Name: Milestone
Manufacturer: Motorola
Form Factor: Slider
Bands/Modes: GSM 850, 900, 1800, 1900 + UMTS 2100, 1900, 850 + GPS
GSM 850, 900, 1800, 1900 + UMTS 2100, 900 + GPS
Memory Internal: 4Gb (512MB) Nand Flash + 2Gb (256MB) mobile DDRam
Memory External: Micro SD (32GB)
Display: 3.7” WVGA (480x854) capacitive Touch screen
Antenna: Internal GSM /UMTS + internal UMTS Diversity + GPS+ BT
TT/SB Time: Talk Time (in minutes): 390min GSM, 290min 3G
Standby Time (in hours): 350hrs GSM, 380hrs 3G
Customer Sync. SW: Motorola Media Link
Available at: Motorola Stores www.motorola.com
Service SW: RSD Net Connected
Available at: My.Motorola.com

## Slide 3
Generic Overview
Connectivity: Micro USB Cable
Data Cable avail. at: www.online-shop.ams-fl.com
Battery Eliminator: BP60
Available at: www.online-shop.ams-fl.com
Flex Flash File Type: 1FF
Required SW: RSD Net Connected
Required Tools: Torque 5, JIS#00 screw driver, heat gun, Tweezers, Black Stick
Mandatory
Repair Fixture: Main Lens Press, Keypad Press, EL panel mylar alignment and press
Cap Press, Alignment Fixture Set
Tools available at: www.online-shop.ams-fl.com
How to update SW: start up RSD Net connected, power up Moblie and connect via Micro
USB cable, start Firmware update process

## Slide 4
Key Selling Points
A “push” based service which extends the experience, always-on social networking to sync up with friends instantly. Be the first to know.
Stay in the loop. Texts, Facebook updates, emails, IMs and phone calls are pushed right to you. See all your conversations in one place & quickly respond on a full QWERTY keyboard and navigate with power of touch.
Great Web to find what you want fast. Search, full HTML browser
720x480 30fps, Video capture and playback
High-Speed - YouTube delivered over HSDPA or Wi-Fi
Google Maps enabled with enhanced GPS; All at your fingertips on a touch 3.7” WVGA screen(480x857).

## Slide 5: Key Features and Enablers
KEY FEATURES AND ENABLERS
Browser: Android Webkit / HTML
Messaging: SMS, MMS, IM, Email (POP, IMAP, IMAP4)
Audio: MIDI, MP3, AAC, AAC+, eAAC+, WAV, WMA v9, WMA v10
Memory: 4/2Gb system, 8GB w/ preloaded MicroSDHC
Phone: Dual mic noise suppression (crystal Talk 2)
Video: 720x480 30fps, Video capture and playback, H.264, MPEG4, WMV
Camera: High Performance 5 MP AF Camera
Other: accelerometer, magnetometer, touch display,
Connectivity: Bluetooth 2.1+EDR w/A2DP, USB2.0 HS, WIFI 802.11b/g
Key Services & Applications
Unique Android UI, centered around your favorites
Social Life Messaging Center – grouping of calls, conversations
(IM, SMS, Email….. )
Connected services – always connected and up to date social network
and news feeds as well as S/W updates

## Slide 6
Product variations
        EMEA, PRC
        Q-Band GSM
        UMTS 900, 2100
        Latin America
        Q-Band GSM
        UMTS 850,1900, 2100

## Slide 7
3,7” Touch Srceen Display
Earpiece Speaker
Mechanical Design Overview
Microphone
Querty Keyboard
Nav.
Key
ON/OFF Key
3.5mm
Headset Con.
5MP AF
Camera
Camera
LED Flash
Micro
USB
Battery
Door
Speaker

## Slide 8
Key Accessories
Desktop Docking Staion

## Slide 9: Level 2 Android Repair Process
Triage1
Triage all incoming units to identify issue
SW Issue
Perform next steps if software issue is identified
HW Issue
Perform next steps if hardware issue is identified
Master Clear
Perform master clear and determine if issue is resolved
(note, user content will be lost)
L2 HW Issue
Repair mechanical issues as needed
L3 HW Issue
SW Update
Perform software update and determine if issue is resolved
Triage
Triage all HW repairs
Return to Customer
If no more issues identified, return to customer
if issue resolved
L3 SW Issue
Android is an open-source operating system which will allow users to download many 3rd party software applications to Motorola Android mobile phones. Due to this support, it’s necessary to update the repair process as indicated in this flow diagram.
User Content Backup2
PIM information done over-the–air by user (Google Sync)
Media information done with Media Link by user (Motorola)
1Perform BLUR login for BLUR enabled phones before Triage
2Recommend user to backup/sync user content before bringing to repair
NTF
Perform RF Go no Go testing
L3 RF issue
Forward to L3/L4 MRSC for further repair
Triage
Triage all SW repairs

## Slide 10: Google Sync
Data Sync access:
From phone, open Menu>Settings> Google synchronization
Choose if you want Auto-sync enabled
Check each application you would like to sync
All synchronization is done over-the-air
Sync Gmail, Calendar, and Contacts from Google to my phone

## Slide 11: Motorola Media Link
Transfer & Sync Photos, Videos, Music with Motorola Media Link
Select USB drive option from phone when data cable is connected
One-click Sync
Motorola Media Link free download available at http://motorola.com

## Slide 12: Dis-Assembly
Please use the Dis-Assembly Manual
Or the Dis-Assembly Video‘s
Available on www.My.Motorola.com