## Slide 1
Milestone

## Slide 2
Generic Overview
Market Name: Milestone
Manufacturer: Motorola
Form Factor: Slider
Bands/Modes: GSM 850, 900, 1800, 1900 + UMTS 2100, 1900, 850 + GPS
GSM 850, 900, 1800, 1900 + UMTS 2100, 900 + GPS
Memory Internal: 4Gb (512MB) Nand Flash + 2Gb (256MB) mobile DDRam
Memory External: Micro SD (32GB)
Display: 3.7” WVGA (480x854) capacitive Touch screen
Antenna: Internal GSM /UMTS + internal UMTS Diversity + GPS+ BT
TT/SB Time: Talk Time (in minutes): 390min GSM, 290min 3G
Standby Time (in hours): 350hrs GSM, 380hrs 3G
Customer Sync. SW: Motorola Media Sync
Available at: Motorola Stores www.motorola.com
Service SW: RSD Net Connected
Available at: My.Motorola.com

## Slide 3
Generic Overview
Connectivity: Micro USB Cable
Data Cable avail. at: www.online-shop.ams-fl.com
Battery Eliminator: BP60
Available at: www.online-shop.ams-fl.com
Flex Flash File Type: 1FF
Required SW: RSD Net Connected
Required Tools: Torque 5, JIS#00 screw driver, heat gun, Tweezers, Black Stick
Mandatory
Repair Fixture: Main Lens Press, Keypad Press, EL panel mylar alignment and press
Cap Press, Alignment Fixture Set
Tools available at: www.online-shop.ams-fl.com
How to update SW: start up RSD Net connected, power up Moblie and connect via Micro
USB cable, start Firmware update process

## Slide 4
Milestone
Memory
Display
Antenna
Connectivity
Alert Speaker
Others
RF
Baseband Chipsets
Camera
Product vs. product
No similar design
Tranceiver IC – TI PMB 5706
BB Processor – OMAP3430
Power Management – TI CPCAP v2.1
512MB Flash /265MB DDRam + ext. Micro SD
3.7” 480x854 capacitive Touch screen
5MP Auto Focus
GSM, UMTS, Diversity, GPS and BT internal
WiFi, BT, Micro USB
16x10mm oval Speaker
Elecronic Compass
Accelerometer
Camera LED Flash

## Slide 5
CPU + Memory (POP) Shield
GPS Shield
Main PCB Top Side Shielding
RF Shield
J5200
Slider Con.
J5150
Side Flex Con.
SD Card
SIM Card

## Slide 6
WIFI, BT, FM Shield
J5100
QWERTY Con.
RF Shield
Main PCB Bottom Side Shielding
El Driver Shield
PM Shield
J7500
Camera Con.

## Slide 7
Main PCB Top Side
Y591
26MHz
J5902
GPS / Diversity Ant.
U100
RX / TX IC
U301
3G ext. LNA
J5901
GSM/ 3G Ant.
J5900
GSM/ 3G to Coax
U6400
GPS receiver
MIC
U1000
U1501
CPU + Memory
(POP)
U8010
Magnetometer

## Slide 8
Main PCB Bottom Side
U5310
EL Driver
U8020
Accelerometer
U2400
PM IC
Y3800
32KHz
U6000
BT, WiFi, FM
U6003
WiFi - PA
U801
FEM +
GSM - PA
U440 / U421
3G - PA

## Slide 9
Slider Flex
Main PCB
Con.
Main PCB
Con.
Touch
Con.
Touch Controler
Ear
Speaker
LCD
Con.
IR sensor for
Face detection

## Slide 10
Power Tree
Click for full view

## Slide 11
Main Chipsets
U801 Front End Module
(GSM PA, Filter, Antenna Switch)
U100 Tranceiver IC
(LNA, Mixer, IF, VCO´s , Exciter, Synthesizer ,Control, B-Band)
U301 LNA
(external 4 stage LNA used for 3G bands)
U401, U421, U440 UMTS PA
  (Single Stage Amplifier for the UMTS Band)
U1000 BaseBand Processor – OMAP 3420
(BB Control, DSP, USB , Codec, USIM, Micro SD, …………)
U1501 BB Processor Memory (POP)
  (512MB Nand Flash, 256MB DDRam)
U2400 Power Management IC – TI CPCAP 2.1
  (Regulators, Charger, Clocks, USB, RTC, SIM Level Shift, ….)
U4990 Microphone Amplifier
U5300 Backlight driver

## Slide 12
U5310 EL Driver
(backlight for QWERTY)
U5320 Camera Flash Driver
U6000 Tranceicer IC
( WiFI, Bluetooth, FM Stereo Receiver)
U6400 GPS receiver
U8010 Magnetometer
(Electronic Compass)
U8020 Accelerometer
(or G-Sensor)
Main Chipsets

## Slide 13: U801 SKY77529
Power Amplifier, GSMK/EDGE Quad-band
Dual line-up power amplifier for GSMK/EDGE (8PSK)
SPI Interface
Power Detection
Harmonic filters
Antenna switch

## Slide 14
Multiband UMTS, WCDMA/EDGE XCVR
U100 SMARTi PMB5706
Fully integrated receiver, transmitter and Synthesis capability.
Five indipendent RF inputs (RX)
Six indipendent RF outputs (TX)
  2 GSM ports
  4 WCDMA ports
Covers all banding combinations for three major regions (US, EU, Japan)

## Slide 15
UMTS PA´s
U401, U421, U440 Skywork
50 OHM Single-band, single-mode WCDMA PA module
Duplex Filter
Power detection
Coupler
Power amplifier
Inter-stage filter
Control Interface

## Slide 16
BaseBand Processor – TI OMAP3420
U1000
The OMAP3420 meets the needs of Multimedia handsets
Integrate an ARM Cortex-A8 superscalar processor – delivering up to 3x the performance of ARM11
+ A8 RISC core
2D/3D graphics accelator
Integrated image signal processor, up to 5MP
Display driver up to WVGA resolution
TV out support, Composite, S-VIDEO
High-speed USB 2.0 On-The-Go support
OpenGL ES2.0 compliant – high level graphic rendering
500MHz
POP archiceture for Memory support

## Slide 17
U1000

## Slide 18
BB Processor external Memory
U1501
4GByte Nand Flash (512MB) + 2GByte DDRAM (256MB) (POP)
Needs for replacement not to be pre-progammed
RAM Address/ Data Bus from/to BB Processor
Flash Address/ Data Bus from/to BB Processor
BB Processor Dual Memor Interface

## Slide 19
Power Management IC TI CPCAP 2.1
U2400
The CPCAP is a custom power/audio management IC
2SPI Control Interfaces
2SSI buses used to carry audio data
10 bit ADC with 16 input chanels
Voice CODEC 16 bit linear dual A/Ds and single channel D/A
16 bit linear Stero DAC
LiIon Battery charger with 20V tolerance input
21 low drop out linear regulators
32.768KHz real time clock system
USB 2.0 HS with OTG and 12 pin SDR ULPI
Lighting controller
Power Cut support
4 Buck and 2Boost regulators

## Slide 20
U2400

## Slide 21
U5300
LED driver with Ambient Light Sensing
The LM3530 is a current mode boost converter. The LED current is adjustable from 0 to 29.5mA via I2C interface. Additional the device features two Ambient Light Sensor inputs, to provide programmable adjustment of the LED current with changes in ambient light.
500KHz switch frequency
1000:1 Dimming Ratio
External PWM Input for simple brightness adjustment
Internal Soft-Start limits Inrush Current
Up to 11 series LED’s
90% Efficieny

## Slide 22
U5310
EL - Driver
The HV861 is a dimmable low Noise Dual EL Lamp driver.
The output voltage is at a nominal value of 90V.
The EL lamp will therfore see ±90V
Adjustable output regulation
Fade-in fade-out capability
Low audible noise
180Vpp output for higher brightness

## Slide 23
U5320
Flash LED driver
The LM3554 is a 2MHz fixed frequency, current mode synchronous boost converter. The divice is a dual 600mA (1.2A total) constant current driver for high current white LED’s
Different operation modes: Torch, Flash, Indicator LED
Programable Flash Timeout
I2C Interface
Programmable current from 37.5mA to 1.2A
Open and Short LED Detection (self protecing)

## Slide 24
Wifi , BT, FM single chip solution
U5600
The TI WiLink 6.0 device integrates an WiFi IEEE 802.11b/g, a BT 2.1+EDR receiver plus
an FM Radio Receiver Module with RDS in one chip solution.
The coexistence features enable simultaneous operation of each integrated function
Designed towork with OMAP processors

## Slide 25
Magnetometer / Electronic Compass
U8010
3-axis geomagnetic measurment
Si-monolithic Hall elements
Wide measurement range such as ± 2000μT
Serial Interface on I2C standard

## Slide 26
Accelerometer
U8020
3-Axes Linear Accelerometer
Capacitiv measurment
I2C Interface
+/- 2g, +/- 4g and +/- 8g dynamically selectable full-scale
2 indipendent programmable interupt generators for free-fall and motion detecion
6D orientation
Embedded self-test
Axes Sensor

## Slide 27
Charger and B_Plus Support
Charger
Charge Transistor
Battery to B_Plus Transistor
I-sense Resistor
Charge process is controlled by TI CPCAP. Temperature contol,
Charege current contol

## Slide 28
Special Solder Skills
None on Milestone
On the Main PCB CPU and Memory are placed as POP.
The memory has not to be preprogrammed
Milestone will not use underfill or underfilm !

## Slide 29: Significant updates
TEST
Modification from GP-Gate HW to Next Test HW (I2C Box is required)
With Android products a new Testhardware will be implemented.
Limited amount of Power Supplies compared to MotoGate at the moment only HP66309D, HP66319D, HP66311B, HP66312A, Keithly 2304, Keithly 2306
Limited amount of Test Sets compared to MotoGate at the moment
8960 and CMU200
Please refer to SER SWT Equipment Standardization.doc